CTRV Model (Constant Turn Rate & Velocity magnitude)
Process Model: { vec x }_{ k+1 }= f( {vec x}_k, {vec %nu }_k )
state: vec x_k= left [ stack{ p_x # p_y # v # %psi # dot %psi } right ]= left [ stack{ x position # y position # speed # yaw angle # yaw rate } right ] noise: {vec %nu }_k= left [ binom{%nu_{a,k}}{%nu_{ddot %psi,k}} right ] {%nu_{a,k}} sim N( 0, { %sigma }_k^{2}) {%nu_{ddot %psi,k}} sim N( 0, { %sigma }_{ddot %psi}^{2})
state transition: {d{vec x}} over {dt}= dot x= left [ stack{ {dot p}_x # {dot p}_y # dot v # dot %psi # ddot %psi } right ]= left [ stack{ v cdot cos(%psi) # v cdot sin(%psi) # 0 # dot %psi # 0} right ] { vec x }_{ k+1 } = { vec x }_k + int from{t_k} to{t_{k+1}} left [ stack{ {dot p}_x(t) # {dot p}_y(t) # dot v(t) # dot %psi(t) # ddot %psi(t) } right ]dt
when {dot %psi}_k<>0 : { vec x }_{ k+1 } = { vec x }_k + left [ stack{{v_k} over {{dot %psi}_k} cdot ( sin( %psi_k + {dot %psi}_k cdot { %DELTA t} ) - sin(%psi_k) ) # {v_k} over {{dot %psi}_k} cdot ( cos( %psi_k ) - cos(%psi_k + {dot %psi}_k cdot { %DELTA t}) ) # 0 # {dot %psi}_k cdot { %DELTA t} # 0} right ] + left [ stack{ {1} over {2} (%DELTA t) ^{2} cdot {cos(%psi_k) cdot { %nu_{a,k} }} # {1} over {2} (%DELTA t) ^{2} cdot {sin(%psi_k) cdot { %nu_{a,k} }} # { %DELTA t } cdot {%nu_{a,k}} # {1} over {2} (%DELTA t) ^{2} cdot {%nu_{ddot %psi,k}} # { %DELTA t } cdot {%nu_{ddot %psi,k}}} right ]
when {dot %psi}_k=0 : { vec x }_{ k+1 } = { vec x }_k + left [ stack{{v_k} cdot cos( %psi_k ) cdot { %DELTA t} # {v_k} cdot sin( %psi_k ) cdot { %DELTA t} # 0 # 0 # 0} right ]

Covariance matrix: Q = left [ binom{{ %sigma }_k^{2}}{0} binom{0}{{ %sigma }_{ddot %psi}^{2}} right ]
Generating Sigma Points:
Start with (x,P) the state and covariance at time step k.
Number of sigma points = 2n_x + 1 where n_x = dim( x )
Sigma points matrix M = left [ x { x + sqrt{( %lambda + n_x )} cdot sqrt{P} } { x - sqrt{( %lambda + n_x )} cdot sqrt{P} } right ]

UKF Augmentation:
augmented state: x_{ a,k } = left [ binom{x_k}{{ %nu }_k} right ] augmented covariance: P_{ a,k }= left [ matrix{P_k # 0 ## 0 # Q} right ]
Calculate augmented sigma points, using augmented state & covariance.

Sigma-point Prediction:
pass each augmented sigma point through the process model

Predict state mean & covariance:
mean: x_{ k+1 } = sum w_i cdot X_{ col(i) } covariance: P_{ k+1 } = sum w_i cdot ( X_{col(i)} - x_{k+1} ) cdot (X_{col(i)} - x_{k+1} )^T
w_1 = {%lambda} over {%lambda + n_a} w_i = {1} over {2(%lambda + n_a)}, i = 2...n_a

Measurement model:
z_{ k+1 } = h( x_{k+1} ) + %omega_{ k+1 }
Compute measurement space sigma points by transforming original sigma points by h.
For example, transform predicted state into radar measurement (range, heading, range rate).
Measurement mean: z_{ k+1 } = sum w_i cdot Z_{ col(i) } covariance: S_{ k+1 } = (sum w_i cdot ( Z_{col(i)} - z_{k+1} ) cdot ( Z_{col(i)} - z_{k+1} )^{T}) + R
where R = E( %omega_k cdot %omega_k^T )

UKF Measurement Update:
Kalman gain: K= T_{k+1} cdot S_{k+1}^{-1} where T_{k+1} = sum w_i cdot ( X_{col(i)} - x_{k+1} ) cdot ( Z_{col(i)} - z_{k+1} )^T
State update: x = x_{ k+1} + K( z - z_{k+1} )
Covariance update: P = P_{ k+1 } - K cdot S_{ k+1 } cdot K^T